## Slide 1: Brownfield to Greenfield: Solar on the Town Landfill
February 2018
Prepared by the Cumberland Climate Action Team
Eric Fitz, Denny Gallaudet, and Jane Wilson
Notes: Jane intro

## Slide 2: Overview
Introduction
Town Electricity Costs
Solar Background
Maine Example – South Portland Landfill Project
Estimated System Size, Costs, and Benefits
Next Steps

## Slide 3: Cumberland Climate Action Team
Founded 2016 by Denny Gallaudet, Eric Fitz, Bob Waterhouse, and Jane Wilson
Combined 100+ years as town residents
Vision: Reduce Cumberland’s carbon footprint by 50% by 2020
Previously presented to the Town Council - August 2016

## Slide 4
Challenge
  The Town spends ~$120k per year
  on electricity
Opportunity
  Reduce costs and source majority of electricity from clean solar energy

## Slide 5: Town Electricity Costs

## Slide 6: Excluding street lighting, ~$70-80k per year is spent across nine town properties.
Chart: Cost By Property – FY 2017
| Town Hall | Valhalla Club | Drowne Rd | Fire Dept | Prince Library | 115 Blackstrap | Valhalla Rd | 187 Tuttle Rd | Blackstrap
 | 214049 | 176125 | 86003 | 64642 | 59321 | 36416 | 24602 | 13283 | 8475
~$25k
$20k

## Slide 7: There are 3 cost components: meter service, demand (kW) and energy (kWh) charges.
Chart: 
| kWh | kW | Meter
Electricty Cost | 57333.8204 | 23023.2737 | 3324
Demand Charge
(kW)
Meter Service Fee
Opportunity to reduce costs
Energy, Transmission
& Distribution (kWh)
60%
Maine regulations allow the town to own and operate a solar system to reduce kWh costs

## Slide 8: Solar Background

## Slide 9
Solar Photovoltaic (PV) = electrical energy

## Slide 10: How does Solar PV work?
DC
AC
1
Solar panels convert sunlight into DC Power
2
Inverter converts DC to AC Power
4
Power flows out to the electric grid
3
A meter records generated energy

## Slide 11: Cumberland has better solar potential than Houston!
US Solar Insolation (Sun Intensity)
Good sun
High local kWh price

## Slide 12: Solar PV is one of the lowest cost options for new utility-scale generation in the US.
Source: Lazard’s Levelized Cost of Energy Analysis Nov 2017
Chart: Average Unsubsidized cost of electricity
| Wind | Solar PV | Gas Combined Cycle | Biomass | Coal
Average | 0.045 | 0.048 | 0.06 | 0.085 | 0.1015

## Slide 13: What happens at night or in the winter?
DC
AC
Net Metering:
A system of utility managed credits and debits on electricity bills
+ 1 kWh
- 1 kWh
5 kWh
1 kWh
Notes: Town is still fully connected to the grid and gets electricity from CMP

## Slide 14: South Portland’s Solar Landfill Project

## Slide 15: Solar PV, sited on closed municipal landfills, are common through out the US and Maine.
South Portland’s capped landfill
Summer 2017
Photo: Courtesy of South Portland

## Slide 16: Solar array structure is ballasted to “float” on the surface of the capped landfill.
Photo: Courtesy of South Portland
Concrete Ballasts

## Slide 17: System is built with simple tools and process.
Concrete Ballasts
Photo: Courtesy of South Portland
Solar Panel Racks

## Slide 18: Mount panels and connect to inverters
Inverter
Photo: Courtesy of South Portland
Mounted Panels

## Slide 19: Estimated System Size, Costs, and Benefits: Cumberland Solar Landfill

## Slide 20: A solar array on Cumberland’s landfill could cover nearly 100% of the town’s usage.
Chart: Estimated Solar Output (500kW array) vs. Town Consumption (non-street light)
| 42552 | 42583 | 42614 | 42644 | 42675 | 42705 | 42736 | 42767 | 42795 | 42826 | 42856 | 42887
Consumption | 61190 | 65376 | 62905 | 55035 | 47144 | 52657 | 64737 | 58598 | 55617 | 52278 | 52647 | 54732
Solar Output | 65973.8984 | 63452.2344 | 56986.3242 | 49507.1992 | 34941.9609 | 34760.0977 | 43293.0312 | 50989.4766 | 61583.7148 | 60318.3242 | 64819.4258 | 61659.6016
Net Metering
Works 24/7 and from season to season.
A well sized system ensures all credits are consumed in a 12 month period.
Usage
Solar Output

## Slide 21
Landfill
Ideal site
Steep terrain
Town Public Works
Approximate scale/location

## Slide 22: There are two common ways of financing a project like this.
Financing
Option A: Town only
Option B: Town + PPA*
South Portland
Free electricity
*PPA = Power Purchase Agreement
1 40 years
7 years
Town purchases electricity from investor via PPA
2
Investor owns
& operates system
1
$1-1.2M
Town buys system at
30 - 45% discount
3
$0.6-0.8M
Town will save up to $2.4M over the life of the system.
Federal Tax Credit
Accelerated Depreciation

## Slide 23: Summary: Brownfield to Greenfield - Solar on the Town Landfill
Maine is a great place for solar
The Cumberland landfill is ideally suited
Estimated savings of up to $2.4M
Save significant taxpayer $ while investing in clean energy

## Slide 24: Additional considerations
Will likely need to extend 3-phase power line
  Approx. $50-$100k cost (included in estimate)
On April 30th, 2018 state regulators are reducing the benefit of net metering
  If paperwork is signed after April 30th, the net metering benefit drops by 10% which would have limited impact on project financials

## Slide 25: Questions and Next Steps